## Slide 1: Development & The US FDA Approval of Generic Drugs
May 18, 2011 | Beijing, China
SHAO Jun, Ph.D.

## Slide 2: Agenda
About Generic Drugs
Business Strategy for Generic Drugs
Generic Drug Product Development
Generic Drug Approval Process
Question-Based Review
Summary

## Slide 3: What are Generic Drugs
US FDA’s Definition:
A generic drug is identical, or bioequivalent to a brand name drug in dosage form, safety, strength, route of administration, quality, performance characteristics, and intended use.

## Slide 4: Generic Share of Market
The global generics market reaches $8.3bn while growth recovers climbing to 7.7%.

## Slide 5: Generic Pharma in U.S.
Generic Prescriptions
  Generic medicines account for 69% of all prescriptions dispensed in the United States, yet only 16% of all dollars spent on prescriptions. (source: IMS Health)
  Generic pharmaceutical products are used to fill nearly 2.6 billion prescriptions every year.

## Slide 6: How Did Generic Drugs Emerge in US Market?
Drug Price Competition and Patent Term Restoration Act of 1984 – Waxman-Hatch Act
  Created a framework for patent term extensions and nonpatent exclusivity periods for brand name drug products
  Created an Abbreviated mechanism for approval of generic copies of all drugs originally approved after 1962, by stating that pre-clinical and clinical testing does not have to be repeated for generics.
  Provided for pre-patent expiration testing (Bolar provision) and generic drug exclusivity

## Slide 7: What are the Basic Requirements?
 Contain the same API as the innovator drug (inactive ingredient may vary)
 Be identical in strength, dosage form, and route of administration to RLD
 Have the same use indications as RLD
 be bioequivalent to RLD
 meet the same batch requirements for identity, strength, purity and quality
 be manufactured under the same strict standards of FDA’s GMP regulations required for innovator products

## Slide 8: Basic Requirements for a Generic Drug
Regulatory & Legal
Labeling
CM&C/Microbiology
Bioequivalence

## Slide 9: When can a Generic Drug be Marketed?
Regulatory & Legal Requirements:
 After patent & exclusivity protection ends, or
 Patent owner waives its rights, and
 FDA requirements are met.

## Slide 10: Regulatory & Legal Requirements
Orange Book:  Approved Drug Products with Therapeutic Equivalence Evaluations  List of drug products approved on the basis of safety and effectiveness by the US FDA under the Federal Food, Drug, and Cosmetic Act.
Patents:  All approved patent numbers and expiration dates  Patents that claim the active ingredients or ingredients  Drug product patents which include formulation/composition patents  Use patents for a particular approved indication or method of using the product
Code (Two-Letter) for Existing Generics:  First letter: if it is bioequivalent; Second letter: Additional information, e.g., dosage forms  Equivalence rating to the innovator product;  If the first letter is A, no biostudy needed for approval (i.e. AA, AN, AO, AP, AT-no problem, AB-demonstrated) - substitutable
 If the first letter is B, NOT to be therapeutically equivalent to other products (BC, BD, BE, BN, BP, BR, BS, BT, BX, B*).

## Slide 11: Regulatory & Legal Requirements
A Certification from ANDA sponsor:  Paragraph I: that such patent information has not been filed;
 Paragraph II: that such patent has expired;  Paragraph III: of the date on which such patent will expire, or

## Slide 12: Regulatory & Legal Requirements
A Certification from ANDA sponsor:  Paragraph IV: that such patent is invalid or will not be infringed by the manufacturer, use, or sale of the new drug for which the application is submitted.
Challenge the listing of the patent; File a statement that the application for use is not claimed in the listed patent; MUST notify the patent holder of the submission of the ANDA. If the patent hold files an infringement suit within 45 days of the ANDA notification, FDA approval for the generic drug is automatically postponed for 30 months.

## Slide 13: Product Insert Label
“Same” as brand name labeling
May delete portions of labeling protected by patent or exclusivity
May differ in excipients, PK data and how supplied
Should use the newest version available
Should use the label from FDA website <drugs@FDA>, rather than DailyMed
Side-by-side comparison is required! Sponsor’s label in SPL format may be provided.

## Slide 14: Chemistry, Manufacture & Control
Components and composition
Manufacturing and controls
Batch formulation and records
Description of facilities
Specs and tests
Packaging
Stability
Microbiology

## Slide 15: CM&C: Product Development
  Decide what product to pursue
  Find source of API (DMF w/US FDA), excipients & packaging materials
  3. Develop a unit formula
  Develop manufacturing process and scale up
  Develop, verify and validate analytical methods
  Set product specification-Control Strategy
  Manufacture submission batches
  Conduct BE study or waive BE study
  Prepare CTD/eCTD and file with US FDA

## Slide 16: What are difference in NDA vs. ANDA Review Process?
Brand Name Drug Generic Drug
NDA Requirements ANDA Requirements
1. Chemistry 1. Chemistry
2. Manufacturing 2. Manufacturing
3. Controls 3. Controls
4. Labeling 4. Labeling
5. Testing & Release 5. Testing & Release
6. Animal Studies
7. Clinical Studies 6. Bioequivalence
8. Bioavailability

## Slide 17: What are difference in NDA vs. ANDA Review Process?
NDA Requirements ANDA Requirements
Stability data Stability data
Three batches One batch
6 M Accelerated 3 M Accelerated and
12 M Storage Long-term storage commitment
Approval Time Approval Time
6 M for priority 6 M cycle*
12 M for standard**
*Median approval times for original ANDA is 18.3 months, 17.3 months and 16.3 months for years of 2002, 2003 and 2004 respectively.
**User fee: 1.5MM.

## Slide 18: Develop A Drug Product
Formulation
Components & Amounts
API Properties
Physical
Chemical
Mechanical
Excipient Properties
Physical
Chemical
Mechanical
Process Steps
Process
Small-scale Manufacture
Scale-up
Validation & Commercialization

## Slide 19: CM&C: Quality by Design
The short version…
QbD is a systematic, science-driven, knowledge and risk based approach to developing, manufacturing and controlling pharmaceutical products throughout their lifecycle.

## Slide 20: CM&C: Quality by Design

## Slide 21: CM&C: Linkage between Q8, Q9 & Q10
Formulation
R&D
Process
R&D
Process Monitoring/
Continuous Verification
Production
ICH Q8(R) Pharmaceutical Dev
ICH Q9 Quality Risk Mngmnt
ICH Q10 Pharmaceutical Quality System

## Slide 22: QbD: Design Space
Multidimensional combination and interaction of input variables (e.g., material attributes) and process parameters demonstrated to provide assurance of quality

## Slide 23: QbD: CMA & CPP
Critical Material Attribute (CMA)
  A physical, chemical, biological or microbiological property or characteristic of a material that should be within an appropriate limit, range, or distribution to ensure the desired product quality
Critical Process Parameter (CPP)
  A process parameter whose variability has an impact on a critical quality attribute and therefore should be monitored or controlled to ensure the process produces the desired quality

## Slide 24: CMAs and CPPs: an Example
Mixing
Compression
Material Attributes
Before Compression
Blend uniformity
Particle size
Density
Moisture
Flow Properties
Process Parameters
Speed
Forces
Depth of fill
Punch penetration depth
Room Moisture
Feeder
Hopper
Material Attributes
After Compression
Tablet weight
Breaking strength
Thickness
UDU
Solid fraction
Friability
Appearance
Identity
Assay
Purity/Impurity
Dissolution
(Disintegration)

## Slide 25: Bioequivalence
A generic drug is considered to be bioequivalent to the RLD if:
 the rate and extent of absorption do not show a significant difference from the listed drug, or
 the extent of absorption does not show a significant difference and any difference in rate is intentional or not medically significant

## Slide 26: What is Bioequivalence?

## Slide 27: Bioequivalence Criteria (Two One-sided Tests Procedure)
AUC and Cmax
  90% Confidence Intervals (CI) must fit between 80%-125%
    Test (T) is not significantly less than reference
    Reference (R) is not significantly less than test
    Significant difference is 20% ( = 0.05 significance level)
      T/R = 80/100 = 80%
      R/T = 80% (all data expressed as T/R so this becomes 100/80 = 125%)

## Slide 28: Waivers of In Vivo Study Requirements
Criteria (21 CFR 320.22)
  In vivo bioequivalence is self-evident
  Parenteral solutions
  Inhalational anesthetics
  Topical (skin) solution
  Oral solution
  Different proportional strength of product with demonstrated BE

## Slide 29: ANDA Approvals
Source: FDA in GPhA Annual Technical Meeting 2010

## Slide 30: Generic Drug Review Process
Sponsor
ANDA
Application Quality Review
Acceptable & Complete
Refuse to Receive Letter
No
Request for Plant Inspection
Chemistry & Micro Review
Labeling Review
Bioequivalence Review
Yes
ANDA#
PreApproval
Inspection Results
OK?
Chem/Micro
OK?
Labeling
OK?
Bioequivalence
OK?
Approval Withheld until Results Satisfactory
No
Deficiency Letters
Deficiency Letters
Yes
Yes
Yes
Yes
No
No
Submission Validation

## Slide 31: ANDA: Question-based Review
Question-based Review (QbR) is a general framework for a science and risk-based assessment of product quality
QbR contains the important scientific and regulatory review questions
ANDA sponsors answer the questions
OGD reviewers evaluate the responses to the questions

## Slide 32: Advantages of QbR
Questions guide reviewers
  Prepare a consistent and comprehensive evaluation of the ANDA
  Assess critical formulation & manufacturing variables
 Questions guide industry
  Recognize issues OGD generally considers critical
  Direct industry toward QbD
 Questions inform readers of the review
  How QbD was used in the ANDA
  Provide the basis for a risk assessment

## Slide 33: Future Generic Industry
      Strong Management
      Control manufacture cost
      Globalization
      Diversified product pipeline
      Biologics- vague and expensive

## Slide 34: Summary
Generic industry has been well established and strictly regulated in the US.
The bar to enter the circle becomes higher in terms of product quality & GPM compliance.
Question-based Review has been used by FDA for generic drug approval & will be required soon.
Generic drug development is a good opportunity for China Pharma to enter global pharmaceutical competition.

## Slide 35: Home of eVenus
Thank you!